## Slide 1
O
O
O
OH
O
O
P
OH
H
CH3
N
CH3
CH3
O
HO
HO
O
HO
HO
O
HO
HO
CH3
CH3
C
H3C
CH3
CH3
OH
NH2
O
HO
O
P
OH
HO
CH3
CH3
C
H3C
CH3
CH3
OH
OH
O
O
O
O
O
O
P
OH
H
CH3
N
CH3
CH3
O
Lipid Imaging Mass Spectrometry.
Advanced Graduate Course in Metabolomics
3-11-2015
Janusz Kabarowski, Dept. of Microbiology, UAB.

## Slide 2
Matrix-Assisted Laser Desorption/Ionization (MALDI):
Matrix molecules absorb laser light, enter an excited state, and collide with sample molecules, facilitating charge transfer to create ions.
Mass Spectrometric Imaging for biomedical tissue analysis
Kamila Chughtai and Ron M.A. Heeren
Chem Rev. Vol.110(5): pp3237–3277, 2010.
MALDI-TOF
instrument
Conventional MALDI plate

## Slide 3
Cryosectioning onto Indium Tin Oxide (ITO) coated glass slides and scanning digital image of slide for “teaching” FlexControl software on MALDI-TOF.
Minimum 2400dpi
cryosection image
Matrix
application
cryosectioning10% gelatin
embedded tissue block
Notes: OCT and other common histological embedding media ionize easily during MS analysis and cause ion suppresion. ITO = indium tin oxide…conductive (must be conductive otherwise electrostatic charges will occur).

## Slide 4
Vacuum sublimation is used to apply an even microscopically thin uniform layer of matrix compound onto tissue section
without the need for solvents.
Sublimation: the transition of a substance from solid to
gas phase without an intermediate liquid phase.
MALDI matrices for lipid imaging:
DHB: 2,5-dihydrobenzoic acid (+ve mode)
1,5-diaminonapthalene (-ve mode)
Notes: The role of the matrix is to absorb the majority of the laser energy leading to explosive desorption of the matrix crystals together with incorporated analyte into the gas phase without degradation of the analyte. The matrix also aids the ionization of analyte molecules in the gas phase due to presence of protons from added acids such as trifluoroacetic acid (TFA).

## Slide 5
How do we apply matrix for MALDI Imaging?
We built a vacuum sublimation apparatus.
Vacuum
micro-valves
Pirani vacuum
gauge
Digital vacuum
monitor
Heated sand bath
Vacuum
sublimation
chamber
vacuum
exhaust
Notes: The Pirani gauge is a thermal conductivity gauge used to measure pressure in vacuum systems. It consists of a metal filament (usually platinum) suspended in a tube which is connected to the vacuum system. A heated metal filament suspended in a gas will lose heat to the gas as its molecules collide with the filament and remove heat…..if the gas pressure is reduced, the number of molecules will fall proportionately and so the filament will lose heat more slowly (measuring the heat loss is thus an indirect measure of pressure).

## Slide 6
Vacuum at 0.05 Torr pressure is required in sublimation chamber and is monitored by electronic Pirani vacuum gauge.
0.05 Torr
750 Torr
(atmospheric pressure)

## Slide 7
Matrix deposition by vacuum sublimation.
Matrix
compound
Cold condensor unit
of vacuum
sublimation chamber
Heated sand
ITO (indium-tin-oxide coated)
slide with cryosections
140°C
0.05 Torr
5-10°C

## Slide 8
Slides with matrix applied by vacuum sublimation.
Deposition of the matrix compound is at the molecular level because gaseous molecules recrystallize at the relatively cold surface of the tissue section attached to the cold condenser.
The uniformity of matrix deposition onto the slide attached to the cold condenser surface reflects the random Brownian motion of the released gaseous matrix molecules.

## Slide 9
Conventional MALDI plate
MALDI plate for cryosections
Adaptated MALDI plate holds slides for MALDI-imaging Mass Spectrometry.

## Slide 10
Setting up a MALDI-IMS run after matrix sublimation.
(2) Regions to image are selected from the
scanned photo of the slide
(1) The slide is placed into a Bruker slide adaptor
and into the MALDI-TOF instrument

## Slide 11
MALDI-IMS in action.

## Slide 12
MALDI-IMS in action.

## Slide 13
How are we applying MALDI-IMS
to our research?
Lipid based mechanisms of immune suppression and anti-inflammatory action by HDL in Lupus.
Acute kidney injury (UAB/UCSD O’Brien Center).
Lipids as mediators of age-related changes in eye lens.

## Slide 14
Zebrafish - an emerging model in biomedical research..
$0.39/tank/day (max fish per tank)
100-200 embryos weekly per sexually mature female
Functional vision by 5 days of age
Transparent embryos permeable to small molecules
Various mutants model human ocular disorders
$0.75/cage/day (max 4-5 mice per cage)
6-8 pups monthly per sexually mature female
Functional vision by 2 weeks of age
Stephen Watts, Ph.D., Department of Biology, Director UAB Aquatic Animal Research Core for NORC.
Notes: Discussing this slide, start with a comparison of the cost and time benefits, then go into a bit of the scientific rationale for zebrafish

## Slide 15
2 month-old Zebrafish
12 month-old Zebrafish
1 month-old Mouse
300mM
300mM
300mM
AGING
12 month-old Mouse
300mM
AGING
Age associated changes in the lens lipidome
of Mouse and Zebrafish.

## Slide 16
Specific aims of the study:
To characterize and compare the lens lipidomes of Mice and Zebrafish.
To analyze the changes that occur in the lens lipdome with aging.
To determine where lipid changes are occurring in the lens.
8 weeks
12 months
2 weeks
12 months
Analyzed using ESI-MS/MS on Triple-TOF Mass Spectrometer
Normalized
weight
6 x 3 lenses
6 x 1 lens
6 x 12 lenses
6 x 5 lenses
Stephen Barnes, Ph.D., Department of Pharmacology & Toxicology, Director UAB TMPL.
Notes: Aims are self explanatory and should be supported by the introduction given before reaching this slide. Bottom portion explains the experimental design. I am only including this much detail because later I will address the drastic difference in intensities, in which case it is important to have mentioned how many lenses were used.

## Slide 17
Precursor mass m/z
Fragment mass m/z
Complete and Comprehensive Data Collection TOF MS Scanning Storing all Product Ions
Q1 selection window 0.5-0.7 amu
Lipidomic Profiling Map of Rat Brain Extracts Acquired in Negative Mode
signal intensity
ESI-MS/MS on Triple-TOF Mass Spectrometer.
Notes: AB-SCIEX 5600 TripleTOF mass spectrometer. This machine, equipped with data-independent Sequential Window Acquisition of all Theoretical mass spectra, generates a comprehensive archive of lipids within an extract for retrospective, quantitative analysis. This technology offers several strengths for delineating unknown pathways.

## Slide 18
Mouse lens positive mode (Total lipids).
0
1
2
3
4
5
6
Log2FC
-log10p
-8
-6
-4
-2
0
2
4
6
8
p˂0.05 (-log10p>1.301)
PG O-44:2 (-PG)
LPC 16:0
PC 36:4 (16:0/20:4)
SM 34:1;3 (LCB 18:2, 2-2H2O, LCB 18:1;3-3H2O)
SM 34:0;4 (SM)
SM 32:3;4 (SM)
PC O-32:1 (PC) [alkyl link]
LPE 12:3 (LPEp)
SM 38:4;2 (SM)
PE 36:0 (-PE)
SM 24:1;2 (SM)
LMMPE 18:0 (-MMPE)
MM(monomethyl) PE 36:0 (-MMPE)

## Slide 19
Zebrafish lens positive mode (Total lipids).
0
2
4
6
8
10
12
-8
-6
-4
-2
0
2
4
6
8
Log2FC
-log10p
PG O-44:2 (-PG)
LPC 16:0
PC 36:4 (16:0/20:4)
SM 34:1;3 (LCB 18:2, 2-2H2O, LCB 18:1;3-3H2O)
SM 34:0;4 (SM)
SM 32:3;4 (SM)
PC O-32:1 (PC) [alkyl link]
LPE 12:3 (LPEp)
SM 38:4;2 (SM)
PE 36:0 (-PE)
SM 24:1;2 (SM)
LMMPE 18:0 (-MMPE)
MM(monomethyl) PE 36:0 (-MMPE)
p˂0.05 (-log10p>1.301)

## Slide 20
p˂0.05 (-log10p>1.301)
Sphingomyelins are increased with ageing in mouse (Black) and Zebrafish (white) lens.
0
2
4
6
8
10
12
Log2FC
-Log10p
-8
-6
-4
-2
0
2
4
6
8
SM
O
O
O
P
OH
CH3
N
CH3
CH3
HO
O
NH
Mouse
Zebrafish
SM 32:3;4
SM 31:2;4
SM 38:4;2
SM 34:0;4
SM 33:2;4
SM 30:2;4
SM 24:4;3
SM 34:1;3
SM 34:1;3
(LCB 18:2;2-2H2O, LCB 18:1;3-3H2O)

## Slide 21
p˂0.05 (-log10p>1.301)
Mouse lens Phosphatidylcholines (white) and Lysophosphatidylcholines (black).
0.0
0.5
1.0
1.5
2.0
2.5
3.0
3.5
4.0
4.5
5.0
-5
-4
-3
-2
-1
0
1
2
3
4
5
36:4 PC
16:0 LPC
Log2FC
-Log10p
O-40:2 PC
42:1 PC
42:3 PC
42:2 PC
42:1 PC
(125m/z MSMS)
30:2 PC ND
22:3 LPC ND
20:3 LPC ND
O-32:1 PC
O-linked acyl PCs only detected
in Mouse
16:0 LPC (125m/z MSMS)
30:1 PC
14:0 LPC
34:5 PC
36:6 PC
LPC
PC
O
O
O
O
O
O
P
OH
H
CH3
N
CH3
CH3
O
O
O
OH
O
O
P
OH
H
CH3
N
CH3
CH3
O
O
O
O
O
O
O
P
OH
H
CH3
N
CH3
CH3
O
1-alkyl, 2-acyl PC

## Slide 22
p˂0.05 (-log10p>1.301)
-Log10p
Zebrafish lens Phosphatidylcholines (white) and Lysophosphatidylcholines (black).
0
1
2
3
4
5
6
7
8
9
10
-7
-5
-3
-1
1
3
5
7
36:4 PC
16:0 LPC
30:2 PC
36:6 PC
34:5 PC
14:0 LPC
22:3 LPC
20:3 LPC
42:1 PC
42:3 PC
42:2 PC
No alkyl (O-) PCs
detected in Zebrafish
30:1 PC
LPC
PC
O
O
O
O
O
O
P
OH
H
CH3
N
CH3
CH3
O
O
O
OH
O
O
P
OH
H
CH3
N
CH3
CH3
O
O
O
O
O
O
O
P
OH
H
CH3
N
CH3
CH3
O
1-alkyl, 2-acyl PC
0
Log2FC

## Slide 23
120
140
160
180
200
220
240
260
280
300
320
340
360
380
400
420
440
460
480
500
520
540
560
580
600
620
640
660
680
700
720
740
760
780
0
500
1000
1500
2000
2500
3000
3500
4000
4500
5000
5500
6000
6500
7000
7500
8000
8500
9000
9500
10000
10500
184.0716
782.5853
783.5896
784.5998
125.0021
Spectrum from MSMSALL_Pos F2.wiff (sample 1) - Pos F-2, Experiment 2, +TOF MS^2 (100 - 1500) from 782.632 min
Precursor: 782.6 Da, CE: 50.0
Intensity
Mass/Charge, Da
ESI-MS/MS fragments from
782.6 m/z 36:4 PC (+mode).
phosphocholine head group
O
O
O
O
O
O
P
OH
H
CH3
N
CH3
CH3
O
0
1
2
3
4
5
6
Log2FC
-log10p
-8
-6
-4
-2
2
4
6
8
p˂0.05

## Slide 24
120
140
160
180
200
220
240
260
280
300
320
340
360
380
400
420
440
460
480
500
520
540
560
580
600
620
640
660
680
700
720
740
760
780
800
820
840
860
880
0
50
100
150
200
250
300
350
400
450
500
550
600
650
700
750
800
850
900
950
1000
1050
1100
1150
790.5569
327.2392
303.2398 FA 20:4
255.2379 FA 16:0
283.2503
792.5702
791.5586
480.3199
328.2431
256.2408
804.5337
343.2343
224.0726
Spectrum from MSMSALL_Neg F2.wiff (sample 1) - Neg F-2, Experiment 2, -TOF MS^2 (100 - 1500) from 840.690 min
Precursor: 840.7 Da
Intensity
Mass/Charge, Da
ESI-MS/MS fragments from
840.7 m/z 36:4 PC acetate adduct (-mode).
O
O
O
O
O
O
P
OH
H
CH3
N
CH3
CH3
O

## Slide 25
So where in the lens are these changes in
16:0/20:4 PC occuring?
Formalin fixed paraffin sections of lens (B) cannot be used for MALDI-IMS (although certain modifications of fixation protocols might allow for subsequent lipid MALDI-IMS). Cryosectioning (after tissue embedding in 10% gelatin) must therefore be optimized for the tissue being studied. In the case of lens, this is very challenging as the dense lens material has a propensity to crack (A).
300mM
300mM
A
B
Tissue processing for matrix application and eye lens MALDI-IMS is challenging
10% gelatin/cryosection H&E
Formalin/paraffin H&E

## Slide 26
A
B
Positive ion mode MALDI average mass spectra of (A) 8 week old and (B) 12 month old Zebrafish eyes, showing the location of the peaks for which images were subsequently taken.
Peaks correspond to expected protonated, sodiated, and potassiated adducts of PC(36:4).
H+ Na+ K+
H+ Na+ K+
8 week old Zebrafish
12 month old Zebrafish
Notes: Figure 7. Positive ion mode MALDI average mass spectra of (A) 8 week old and (B) 14 month old zebrafish eyes, showing the location of the peaks for which images are shown in (C).

## Slide 27
[PC(36:4)+H]+ = 782.6
[PC(36:4)+Na]+ = 804.6
[PC(36:4)+K]+ = 820.5
8 weeks old
12 months old
MALDI-IMS on protonated, sodiated, and potassiated adducts of PC(36:4) in zebrafish eye.
Notes: Peaks correspond to expected protonated, sodiated, and potassiated adducts of PC(36:4).

## Slide 28
120
140
160
180
200
220
240
260
280
300
320
340
360
380
400
420
440
460
480
500
520
540
560
580
600
620
640
660
680
700
720
740
760
780
800
820
840
Mass/Charge, Da
184.0787
782.5876
783.5930
784.6038
599.5165
125.0026
146.9849
185.0812
723.5085
100 200 300 400 500 600 700 800
choline head group
parent ion
MS/MS on m/z 782.6 shows fragmentation indicative of PC(16:0/20:4)
Mass/Charge (m/z), Da
8 weeks old ZF
12 months old ZF
m/z
782.6
MS/MS on protonated adduct of PC(36:4) in Zebrafish eye.
O
O
O
O
O
O
P
OH
H
CH3
N
CH3
CH3
O
Notes: MALDI-IMS MS/MS analysis (DHB matrix, + mode) of PC(16:0/20:4) in zebrafish lens.

## Slide 29
OLD MOUSE LENS #2
(9-5-2014)
16:0/20:4 PC
MALDI-IMS on 16:0/20:4 PC(36:4) in mouse eye.
16:0/20:4 PC

## Slide 30
1 year old MOUSE LENS #2 (9-5-2014)

## Slide 32
TOTAL EYE spectrum
Restricted diacyl phospholipids in lens core.
LENS CORE spectrum
↑
↓
LENS PERIPHERY spectrum
LENS PERIPHERY spectrum
Mouse eye, 9-5-14

## Slide 33
Quantitative and Spatial
Analysis of Lipids Involved in
Acute Kidney Injury.

## Slide 34
Specific aims of the study:
1) To characterize the kidney lipidome of mice following acute injury (quantitatively).
Sham
IR
Analyzed using ESI-MS/MS on 5600 Triple-TOF Mass Spectrometer
Normalized
kidney weight
8-10 weeks
old C57Bl6/J
Notes: AB-SCIEX 5600 TripleTOF mass spectrometer. This machine, equipped with data-independent Sequential Window Acquisition of all Theoretical mass spectra, generates a comprehensive archive of lipids within an extract for retrospective, quantitative analysis. This technology offers several strengths for delineating unknown pathways.

## Slide 35
signal intensity
Lipidomic Profiling Map of Rat Brain Acquired in Negative Mode
storing all product ion spectra; 1.6 min
Precursor mass m/z
Fragment mass m/z
MS/MS of Every Precursor
Product Ion Scan of Every Lipid
ESI-MS/MS on Triple-TOF Mass Spectrometer.

## Slide 36
Specific aims of the study:
MALDI-Imaging MS on a Bruker-TOF Mass Spectrometer
Kidney cryosections
2) To analyze WHERE the changes in lipids occur in the kidney (spatially) and to characterize those lipids that remain unchanged quantitatively but might be spatially altered.
Sham
IR
8-10 weeks
old C57Bl6/J

## Slide 37
Sham or IR left kidney
nephrectomy
6 hours reperfusion
Euthanization…
PBS/BHT perfusion
30 mins
renal ligation
Kidney homogenization
in 1ml PBS/BHT
Samples
under Argon
Dried lipids
under Argon
SWATH 5600 TOF
-80°C
Resuspend lipids in MetOH
Extract lipids (Bligh Dyer)
In vivo mouse model of AKI:
½ Kidney homogenization
in 1ml PBS/BHT
MALDI-IMS
½ Kidney 10% gelatin embedding
IR (0.5/24hrs) plasma
creatinine 1-2mg/dL
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
Plasma creatinine (mg/dL)
SHAM control
IR (0.5/6 hrs)

## Slide 38
p˂0.05
(-log10p>1.301)
Mouse kidney lipids changed following IR (0.5/6hrs)
(5600 Triple-TOF SWATH
positive mode).
0.5
1.0
1.5
2.0
2.5
3.0
-15
-10
-5
0
5
10
15
-log10p
Log2FC
8-10 weeks old C57Bl6/J (n=6)
PE O-40:5
780.6_639.6
GT2 26:0;2
(LCB 18:0;2-H20)
900.8_284.3
PE O-40:4
782.6_641.6
GD2 32:2;2
(LCB 18:2;2-H20,
LCB 18:1;3-3H2O)
900.8_284.3
PC O-38:1
802.7_184.1
SM 39:3;2
769.7_184.1
CE 27:3 +NH4 (chol)
790.7_369.4
LPC 22:6
568.4_184.1
PE O-42:3
812.7_198.1

## Slide 39
p˂0.05 (-log10p>1.301)
0.5
1.0
1.5
2.0
2.5
3.0
3.5
4.0
-8
-6
-4
-2
0
2
4
6
8
Mouse kidney lipids changed following IR (0.5/6hrs)
(5600 Triple-TOF SWATH negative mode).
-log10p
Log2FC
8-10 weeks old C57Bl6/J (n=6)
PC 16:0/18:2
844.8_255.2
LPI O-28:0
725.5_223.0
PE 46:2
882.8_196.0
PE 46:2
882.8_196.0
PE O-14:0/20:4
696.5_303.2
PE 14:0/20:4
710.5_227.2
PE O-40:1
786.7_196.0

## Slide 40
O
O
O
O
O
O
P
OH
H
NH2
O
1-alkyl, 2-acyl PE
Plasma creatinine (IR 0.5/6hrs)
PE O-40:4 intensity
r=0.771
p=0.00228
O
O
O
O
O
O
P
OH
H
O
NH2
1-acyl, 2-acyl PE
Plasma creatinine (IR 0.5/6hrs)
PE O-40:5 intensity
r=0.724
p=0.0062

## Slide 41
r=0.730
p=0.0062
O
O
O
O
O
O
P
OH
H
N
O
1-alkyl, 2-acyl PC
CH3
CH3
CH3
O
O
O
O
O
O
P
OH
H
O
1-acyl, 2-acyl PC
N
CH3
CH3
CH3
PC O-38:1 intensity
r=-0.695
p=0.0121
SM O-39:3;2 intensity
Plasma creatinine (IR 0.5/6hrs)
Plasma creatinine (IR 0.5/6hrs)

## Slide 42
CE 27:3 +NH4 (chol) intensity
r=0.886
p=0.0333
r=-0.582
p=0.0446
GD2 32:2;2 intensity
Plasma creatinine (IR 0.5/6hrs)
Plasma creatinine (IR 0.5/6hrs)

## Slide 43
SHAM control
IR (0.5/6hrs)

## Slide 44: MALDI-IMS on PE O-40:4 (782.6_641.6)
0.5
1.0
p˂0.05 (-log10p>1.301)
IR
SHAM
1.5
2.0
2.5
3.0
-15
-10
-5
0
5
10
15
-log10p
Log2FC
PE O-40:5
780.6_639.6
PE O-40:4
782.6_641.6

## Slide 45
Stephen Barnes
Landon Wilson
Ray Moore
UAB, Targeted Metabolomics and Proteomics Lab
David Graves
UAB, Chair Department of Chemistry
Anupam Agarwal
UAB, Dept Medicine, O’Brien Acute Kidney Injury Research Center
Trenton Schoeb
UAB, Dept Genetics, Dir. Comparative Pathology Core Laboratory
Acknowledgments.
Miranda Collier
UAB, Honors and Chemistry Scholars Undergraduate Fellowship Program
(Currently Ph.D University of Oxford)
Alex Johnson
Kelly Walters
UAB, Undergraduate Chemistry (Pre-Med)
Sangeetha Rao
UAB Resident
Steve Burgess
Dir. R&D, Avantipolar Lipids